## Slide 1: Depth Estimation Based on Monocular Image for the Moon With Machine Leaning and Shape-From-Shading s1270087 IBUKA. Koichiro, Supervisor: Prof. DEMURA. Hirohide
1. Introduction
2. Methodology
3. Current Status
Digital Terrain Models (DTMs) of the lunar surface are widely used for lunar exploration planning and studies of topography and geology [1]. LRO NAC DTMs with the highest resolution (~2 m/pix) cover small percentage with 470 pieces [2] . This is due to the time required to create DTMs by manual and the few data available to create them [3].
The purpose of this study is to generate high-resolution DTMs automatically with limited data. This research proposes a method to complement LRO NAC DTMs by generating the almost the same resolution using Machine Learning & Shape-From-Shading (SFS) [4]. The goal of this study is to implement a pipeline generate DTMs that combines machine learning with SFS and evaluate the generated DTM.
Figure 1 shows flowchart of Methodology in this research. We use a Pix2Pix [5] as machine learning model. This model can transform the type of image by learning the relationship between two sets of images. DTMs can be generated from abundant visible images by training Pix2Pix on both DTMs and visible images.
SFS is a technique for estimating the shape of an object from a single shaded image. We improve DTMs generated from Pix2Pix adapting SFS.
Figure 2 shows the process of creating Pix2Pix training data. This research select SLDEM 2015 [6] & LRO NAC Orthoimage [7] as dataset. First, LRO NAC Orthoimages are downsampled to match the resolution of SLDEM 2015. Next, the images are cut and shaped to 256x256 pixel. Finally, histogram smoothing is applied to images and aligned into a 512x256 pixel image.
References
4. Schedule
[1] Barker, M. K., et al., A new lunar digital elevation model from the Lunar Orbiter Laser Altimeter and SELENE Terrain Camera, 2016. doi:10.1016/j.icarus.2015.07.039
[2] Henriksen, M., et al., LROC NAC Digital Terrain Models: Production and Availability, 2020. In Proceedings of the Lunar Surace Science Workshop, virtual meeting, 28–29 May 2020; LPI Contribution 2241. p. 5084.
[3]Onodera, K., et al., Resolution enhancement of DEM of the lunar surface using machine learning, 2020. doi:10.20637/JAXA-RR-19-006/0003
[4] Horn V. K. P. & Brooks M. J., SHAPE from SHADING, (London, MIT Press,1989).
[5] Isola, P., et al., Image-to-Image Translation with Conditional Adversarial Networks, 2016. doi:10.1109/CVPR
[6] http://imbrium.mit.edu/EXTRAS/SLDEM2015/
[7] https://wms.lroc.asu.edu/lroc/rdr_product_select
Figure 1. Flowchart of Methodology
SLDEM 2015
LRO NAC Orthoimage
Cut & histogram smoothing
Figure 2. Preprocessing dataset
1/10
LPSC abstract deadline
1/20
GT draft deadline
2/15,16
GT Presentation
3/13 ~ 17
LPSC Presentation
Notes: reference 行間狭める
図版はは本文で言及する
数値地形空間か画像空間にSFSをやるのかがわからない
Fig1が分かりづらい
SFSをどう使うかに書く